# Compiling a working GNU toolchain under Windows
## Introduction
Compiling a GNU toolchain under Windows can be a pain in the ass. The special challenge lies in getting the include directory pathes relative, so that relocating the toolchain is possible without hacking the tool flags.
While this is automated for ReactOS through the buildtoolchain.sh script now, I'm giving some hints here for manually compiling it, so you don't run into the same problems I have gone through. This can also be useful for compiling a later version of the tools if my script should fail for them.
## General notes
 Use MSYS as the build environment for this tutorial
While Cygwin might look like a better alternative for getting the include directories right (since it doesn't do implicit path translation), you can only build a mingw32 compiler as a cross compiler with it. This is not what we want to do here (and it probably gets us into many other problems).

 MSYS does an implicit path translation
MSYS implicitly translates Unix pathes (like /mingw) to their Win32 equivalents. While this usually helps, it can get you into serious trouble when trying to get the built-in include directories relative in gcc.
A way to avoid such a translation is passing a Win32 path with Unix slashes (like c:/buildtoolchain). I currently do this for the --prefix parameter when compiling gcc. Still, this doesn't work well for the whole compilation process, so other hacks are necessary (see Specific problems section).

 Don't build a cross compiler
Specifying --target=mingw32 without --host=mingw32 will compile the build tools as cross compilers, because the implicit values for these variables are i686-pc-mingw32 and a cross compiler will always be built if the values are not exactly the same. This usually gets you into even more troubles, so avoid building a cross compiler.
It's the easiest here to drop --host and --target parameters entirely, they will be set to i686-pc-mingw32 automatically then.
## Specific problems
 make fails with The directory that should contain system headers does not exist
The mingw-runtime and w32api headers and libraries must go to their appropriate subdirectories in /mingw. No other path is possible here, this one is hardcoded into gcc.

 make fails with error: stdio.h: No such file or directory when running xgcc
The headers and library files of mingw-runtime and w32api also need to go to their appropriate subdirectories in the target subdirectory of the prefix directory (e.g. c:/buildtoolchain/mingw/i686-pc-mingw32) in addition to /mingw.

 make fails with *** target pattern contains no `%'. Stop.
The ORIGINAL_LD_FOR_TARGET variable was probably set wrong due to MSYS' path translation not working well here. You can work around this problem by adding --with-ld=/bin/ld to the parameters of the gcc configure script.

 make install fails with tar: unable to record current working directory
This is a problem in the current tar version of MSYS 1.0.10 (see here). Please download the latest preview version of tar from the MinGW project page and try again.